## Slide 1
Srikar C
S20220010207
RURAL HEALTHCARE DATA ANALYSIS
WARDHA, MAHARASHTRA ,INDIA
Parth Vijay
S20220010166
Group - 6
COURSE INSTRUCTOR: DR.ARUN P.V

## Slide 2
INTRODUCTION
  Rural healthcare access is often hindered by poor infrastructure and geographical barriers.
  Spatial data helps us analyze terrain, settlement patterns, and proximity to medical facilities.
  Significance: Supports policy-making, infrastructure development, and emergency planning.
  Title: Improving Rural Healthcare Accessibility Using Geospatial Analysis

## Slide 3
PROBLEM STATEMENT &
OBJECTIVES
  Identify underserved areas.
  Evaluate proximity of PHCs, hospitals to roads and settlements.
  Assess environmental factors affecting accessibility.
  Integrate raster and vector layers for multi-criteria analysis.
Lack of spatial insight into rural healthcare facility accessibility and support systems.
Reference Research paper:-Abulibdeh, A., Alshammari, H., Al-Hajri, N. et al. Geospatial Assessment of Healthcare Accessibility and Equity in Qatar in Preparation for the 2022 FIFA World Cup. J geovis spat anal 9, 2 (2025). https://doi.org/10.1007/s41651-024-00206-z

## Slide 4
01
02
03
STUDY AREA & DATASETS
STUDY AREA : WARDHA EAST AND WEST , MAHARASHTRA
VECTOR LAYERS: ROADS, HOSPITALS, RIVERS, PHCS, WATER BODIES, RESIDENTIAL COMPLEXES, FORESTS, NURSING SCHOOLS, PHARMA LABS, BOUNDARY
RASTER LAYERS: VEGETATION, LAND COVER, POPULATION, ELEVATION, TEMPERATUREWARDHA EAST AND WEST , MAHARASHTRA

## Slide 5
DATASET COLLECTION
PREPROCESSING
VISUALIZATION & OUTPUT
Gathered vector and raster datasets including roads, health facilities, water bodies, land cover, and elevation from government portals and remote sensing sources.
Cleaned, reprojected, and clipped datasets to the study boundary; normalized raster layers for uniform analysis.
Raster overlays for spatial suitability and executed spatial queries to analyze healthcare accessibility and infrastructure support.
Generated thematic maps and statistical insights using QGIS to present optimal locations and infrastructure connectivity for rural healthcare planning.
RASTER OVERLAY & VECTOR QUERIES
OVERALL METHODOLOGY

## Slide 6
VEGETATION-NDVI
RASTER LAYERS
TEMPERATURE
LAND COVER
ELEVATION
POPULATION

## Slide 7
VECTOR LAYERS - I
LAYERS:-
  Boundary(Green)
  Forest(Purple)
  River(Red)
  Roads(grey)
  Hospitals(yellow polygon)
  Viral disease spots

## Slide 8
VECTOR LAYERS - II
LAYERS:-
  Pharma(orange)
  P.H.C(green)
  Nursing(yellow)
  Water body(blue)
  Residential(brown)
  WaterBorne disease

## Slide 9
QUERIES AND ANALYSIS
01
RASTER-BASED HEATMAP ILLUSTRATING ACCESS TO RURAL HEALTHCARE.
Weighted sum of 5 normalised raster layers
    low elevation -0.25
    low vegetation-0.25
    high land cover-0.20
    high temperature-0.20
    high population-0.10
RASTER

## Slide 10
02
QUERIES AND ANALYSIS
OPTIMAL NEW HEALTHCARE FACILITIES
Finds residential buffer areas not served by nearby healthcare or roads but intersecting green spaces.
Highlights potentially underserved yet environmentally favorable zones for development or intervention.
VECTOR QUERY
(RES_BUFFER - (HEALTHCARE_BUFFER ∪ ROAD_BUFFER)) ∩ GREEN_BUFFER

## Slide 11
ESTIMATION OF NEEDED ROAD NETWORK
VECTOR QUERY
03
Identifies healthcare facilities (PHCs, hospitals, nursing homes, pharmacies) located away from road networks.
Subtracts road buffer zones to highlight less accessible or remotely located facilities.
QUERIES AND ANALYSIS
(PHC ∪ HOSP∪ NURSING ∪PHARMA)-BUFFER(ROADS)

## Slide 12
QUERIES AND ANALYSIS
04
CONSTRUCTION OF NEW HOMES WITH HEALTH ACCESS
Identifies healthcare facilities (PHCs, hospitals, nursing homes, pharmacies) outside residential buffer zones.
Clips the result to the administrative boundary to focus on the area of interest.
VECTOR QUERY
CLIP( (PHC ∪ HOSP∪ NURSING ∪PHARMA)-BUFFER(RESIDENTIAL)) BOUNDARY

## Slide 13
QUERIES AND ANALYSIS
05
WATERBORNE DISEASE RISK ZONES
Extracts waterborne disease cases that fall outside the influence zones of healthcare and residential buffers.
Applies symmetric difference to highlight underserved or potentially neglected risk areas.
VECTOR QUERY
SYM_DIF(WATERBORNE CASES- BUFFER(HEALTHCARE U RESIDENTIAL))

## Slide 14
QUERIES AND ANALYSIS
06
VIRAL SPREAD IN HIGH POPULATION AREAS
Identifies viral disease cases located near healthcare facilities and residential areas.
Uses intersection of reported cases with a buffer around healthcare and residential zones.
VECTOR QUERY
INTERSECTION(REPORTED VIRAL CASES & BUFFER(HEALTHCARE U RESIDENTIAL))

## Slide 15
QUERIES AND ANALYSIS
07
OPTIMAL LOCATION FOR PHC
Placing new PHCs to improve healthcare accessibility in underserved neighborhoods
VECTOR QUERY
BUFF(RESIDENTIAL-ROAD)

## Slide 16
QUERIES AND ANALYSIS
08
PRIORITY ZONES FOR HEALTHCARE ZONES
VECTOR QUERY
Hospitals & PHCs → 2 km buffer
These are areas with coverage; we'll exclude them.
Residential Complexes → 2 km buffer
We want to serve areas close to where people live.

## Slide 17
QUERIES AND ANALYSIS
09
PRIORITY ZONES FOR HEALTHCARE ZONES
Roads → 1 km buffer
Represents areas that are road-accessible.
Water Bodies & Forests → 1 km buffer
Exclusion zones (not ideal for setting up a facility).
VECTOR QUERY

## Slide 18
QUERIES AND ANALYSIS
10
PRIORITY ZONES FOR HEALTHCARE ZONES
Exclusion Zones
Union water_body_buffer and forest_buffer
Then subtract this union from the study area boundary:
Difference → Input: boundary, Overlay: exclusion_zones
Expression : Boundary_Polygon - (Water_buffer U Forest_Buffer)
VECTOR QUERY

## Slide 19
QUERIES AND ANALYSIS
11
PRIORITY ZONES FOR HEALTHCARE ZONES
Covered Zones (served by existing hospitals/PHCs)
Union hospital_buffer and phc_buffer → Output: served_area
Expression : Boundary_Polgon - (Hospital U PHC)
VECTOR QUERY

## Slide 20
QUERIES AND ANALYSIS
12
PRIORITY ZONES FOR HEALTHCARE ZONES
Hot-Spot Identification
The result highlights hotspot zones where healthcare facilities can be prioritized because they are both buildable and close to residential populations.
Expression : Buildable_Area ∩ Residential_Complex
VECTOR QUERY

## Slide 21
  Relevance: Over 65% of India’s population lives in rural areas, yet access to healthcare remains limited due to poor infrastructure and distance.
  Who’s Working: Organizations like NITI Aayog, NHSRC, and private players like WISH Foundation are actively researching and addressing gaps.
  Technology Use: Satellite data (like ISRO’s Bhuvan & NASA’s Night Lights) and GIS tools (QGIS, ArcGIS) help map underserved regions.
  Recent Trends: Mobile health units, telemedicine, and AI-driven health mapping are emerging to improve rural reach.
MARKET RESEARCH

## Slide 22
THANK YOU